## Slide 1
Zephyr Workshop – Kconfig + DeviceTree
Understanding how Zephyr RTOS configures features and hardware

## Slide 2
What is Kconfig?
Configuration system for:
System features
Drivers
RTOS options
Options start with 'CONFIG_'

## Slide 3
Kconfig – How it Works
prj.conf
CONFIG_PRINTK=y
CMake + Kconfig
Build system processing
Header Files
Generated configuration
Use 'west build -t guiconfig' to explore

## Slide 4
What is DeviceTree?
Hardware description language that:
Describes hardware layout and connections
Used by Zephyr at build time to generate hardware abstraction code.
Files: *.dts (base), *.overlay (app-level override)

## Slide 5
DeviceTree Concepts
Nodes
Hardware blocks (e.g., &gpio0)
Properties
Configuration data (pins, levels)
Labels & Aliases
Simplified code access

## Slide 6
How Kconfig & DeviceTree Work Together
Kconfig
Enables drivers (CONFIG_GPIO=y)
DeviceTree
Defines hardware (LED on GPIO0, pin 13)
Application
Uses enabled, defined hardware

## Slide 7
Live Example – LED Blink
Start with Hello World
Base project structure
Edit Files
prj.conf and main.c
Add app.overlay
Define LED alias

## Slide 8
prj.conf – Example
CONFIG_GPIO=y
Enables the GPIO driver subsystem

## Slide 9
app.overlay – Example
/ {
aliases {
led0 = &led0;
};
};
Defines hardware reference for LED

## Slide 10
main.c – DeviceTree Usage
Add the code from blinky led sample to main.c

## Slide 11
Run the sample
build and flash on nrf52dk
files .dts and _defconfig from the folder boards/nrf52dk generates the configuration
Check the file build/zephyr/.config
Check the file build/zephyr/zephyr.dts

## Slide 12
Explore menuconfig
Run: west build -t guiconfig
Enable or disable options
Compare output with build/zephyr/.config now