## Slide 1
Zephyr Workshop - Sensor Subsystem
A comprehensive introduction to Zephyr's sensor abstraction layer, featuring practical implementation with the TMP102 temperature sensor.

## Slide 2
What is the Sensor Subsystem?
The Sensor Subsystem in Zephyr RTOS provides:
A generic interface to interact with various sensor hardware regardless of manufacturer
Portable application code that works across different sensor implementations
Unified API for accelerometers, gyroscopes, temperature sensors, and many more

## Slide 3
Why Abstraction Matters
Vendor-Agnostic
Switch between sensor hardware without rewriting application logic, enabling easy hardware upgrades
Simplified Architecture
Reduces complexity in the application layer by hiding implementation details
Consistent Pattern
Universal workflow: fetch → get channel → process data
This abstraction is particularly valuable in embedded systems where hardware configurations change frequently during development.

## Slide 4
Sensor Driver API Overview
sensor_sample_fetch()
Initiates a sensor reading operation, gathering fresh data from the hardware
sensor_channel_get()
Retrieves specific channel values from the most recent fetch operation
sensor_attr_set()
Optional: Configure sensor attributes like scale, frequency, and sensitivity
sensor_trigger_set()
Registers interrupt handlers or polling callbacks for sensor events

## Slide 5
Zephyr Sensor Channels
Zephyr defines standard channel types that represent different sensor measurements:
SENSOR_CHAN_ACCEL_XYZ
3-axis acceleration data, typically in m/s²
SENSOR_CHAN_GYRO_XYZ
3-axis angular velocity, typically in rad/s
SENSOR_CHAN_TEMP
Temperature readings in degrees Celsius
SENSOR_CHAN_LIGHT
Ambient light levels, often in lux
SENSOR_CHAN_PRESS
Atmospheric pressure, typically in kilopascals
Each channel type corresponds to a specific type of physical measurement that can be retrieved from compatible sensors.

## Slide 6
Sensor Value Struct
struct sensor_value { int val1; /* integer part */ int val2; /* fractional part in micro units */};
For example, to represent 20.500000°C:
val1 = 20 (integer part)
val2 = 500000 (fractional part)
Typical usage in code:
printf("%d.%06d", val.val1, val.val2);
This representation allows for precise readings while avoiding floating-point operations, which can be expensive on embedded systems.

## Slide 7
TMP112 Implementation of Sensor API
The TMP112 temperature sensor demonstrates how to implement the Zephyr sensor API:
Extends the generic sensor driver interface
Implements required callbacks for initialization
Provides channel-specific data retrieval
Translates raw sensor values to standard format
Key files to examine:
include/zephyr/drivers/sensor.h - API definition
drivers/sensor/tmp112/tmp112.c - Implementation example

## Slide 8
What is Required in DeviceTree?
1
Sensor Description
Sensor must be properly described in the board's .dts file or in an application-specific overlay file
2
Bus Connection
Specify the connection method (typically I2C or SPI) with correct bus parameters
3
Required Properties
Include the "compatible" string to match driver, "reg" for address, and any GPIO interrupt connections

## Slide 9
Sample Demo: TMP102 Setup
To prepare the TMP102 demo:
Navigate to the sample directory: samples/sensor/tmp112
Create an app.overlay file for your board
Update the arduino_i2c node from nrf52dk_nrf52832.dts
Add the TMP102 sensor node with appropriate address
Hint: TMP102 is similar to TMP112 but uses a different I2C slave address. Check frdm_k64f.overlay for reference.

## Slide 10
Sample Demo: Building and Testing
Build the Sample
Use the west build command to compile the sample for your target board:
west build -p always -b nrf52dk/nrf52832 samples/sensor/tmp112
Connect Hardware
Wire the TMP102 sensor to the development board according to the pinout documentation.
Flash and Test
Upload the firmware and verify operation:
west flash
Monitor the serial output to confirm temperature readings.

## Slide 11
Shell Integration
Zephyr allows registering CLI commands via shell subsystem
comment out the do_main function
add to prj.conf
CONFIG_SHELL=y CONFIG_SENSOR_SHELL=y
rebuild and flash
run ‘sensor get tmp112@48 ambient_temp’

## Slide 12
zephyr abstraction
change zephyr board to nrf52833/40 or stm32wl
rebuild and run