## Slide 1: USB Subsystem
Target board: nRF52840 DK
Run HID and RNDIS samples

## Slide 2: What is USB in Zephyr?
Zephyr supports USB device functionality
Classes include: CDC ACM, HID, RNDIS, Mass Storage

## Slide 3: Common USB Use Cases
Serial over USB (CDC ACM)
Custom USB devices (HID, vendor-specific)
USB networking (ECM, RNDIS)
Firmware updates (DFU)

## Slide 4: HID Sample (Human Interface Device)
Path: samples/subsys/usb/hid
Simulates mouse or keyboard
Device appears as USB HID class

## Slide 5: Build & Flash HID Sample
west build -b nrf52840dk/nrf52840 samples/subsys/usb/hid-mouse
west flash

## Slide 6: RNDIS (USB Ethernet)
Device presents itself as virtual Ethernet interface
Can communicate with host as if over network

## Slide 7: Create rndis app
Copy the hid sample
Remove the following files:
  README
  .yaml file
  usbd_next_prj.conf

## Slide 8
CmakeList file:
  Change the project to rndis
.overlay:
  &zephyr_udc0 {
  rndis_func: rndis {
  compatible = "zephyr,usb-rndis";
  };
  };

## Slide 9
Use the files main.c to create network interface
Use the file prj.conf to enable all the relevant configs

## Slide 10: Demo Steps
Build and flash
Check with `dmesg` and `ip addr` on host
Configure the interface to 2.2.2.1/255.255.255.0
Try to ping from the host and from zephyr shell

## Slide 11: Telnet
Add telnet server as backend in prj.conf
  CONFIG_SHELL_BACKEND_TELNET=y
  CONFIG_SHELL_TELNET_SUPPORT_COMMAND=y
Connect from the host to telnet and run the shell
  Telnet 2.2.2.2